## Slide 1
Confined Space Training
“Attendant”
Designed for employees who serve as attendants
under the permit required confined space program.
Effective Date: February 28, 2019
Notes: The objective of the site Confined Space Entry program is to have a system for identifying Confined Spaces, evaluating the potential hazards associated with these spaces and developing hazard controls and safe entry procedures. The Confined Space program shall provide systematic approaches to protect employees from hazards associated with working inside equipment or other places with limited room or access. Whenever possible, Confined Space work shall be avoided, but when it is necessary, strict adherence to the provisions of this program is required.

## Slide 2: Course Objectives
The goal of this course is to help the Attendant to understand their role in creating a safe, permit-required confined space entry.
Our aim is to provide each student with the knowledge, tools, procedures and specific processes that will ensure all permit-required confined space entries are conducted safely.
Prerequisite: Entrant Training

## Slide 3: Attendant General Duties
Stationed Outside
May not leave post for any reason
Performs Attendant Duties
No use of cell phone or texting
No reading of books or newspapers
Constant communication with entrants

## Slide 4: Attendant
An Attendant is stationed outside of each permit-required confined space during entry operations and remain in contact with the authorized entrants.
Attendants will be trained in the use of atmospheric monitoring equipment.
Attendants will maintain an accurate count of all authorized entrants in the space.
Attendants must recognize potential hazards inside and outside of the space and determine if Authorized Entrants should evacuate.

## Slide 5: Attendant
Communication
  Attendants shall maintain effective and continuous contact with Authorized Entrants during entry.
  The Attendant will summon rescue and other emergency services as soon as the attendant determines that authorized entrants need to escape from permit-required confined space hazards.

## Slide 6: Attendant
Communication
  Attendants shall order Authorized Entrants to evacuate when they observe a hazardous condition which is not allowed in the entry permit such as:
    Detection of behavior effects of hazard in the permit space.
    Detection of outside situations which could endanger an entrant.
    Detection of an uncontrolled hazard within the permit space.
    The Attendant must leave the work station
    The Attendant loses contact with authorized entrants during entry

## Slide 7: Attendant
Communication
  The Attendant will take the following action when unauthorized person(s) approach or enter a permit space while entry is underway:
    Warn the unauthorized person(s) away from the space
    Request the unauthorized person(s) to exit immediately if they have entered the space.
    Inform the authorized entrants that unauthorized person(s) have entered the space.

## Slide 8: Attendant
Communication
  Attendants will take control over and secure gas-cutting, welding, or arc welding equipment in the event of an emergency.
  Attendants will constantly monitor the ventilation system to ensure adequate working conditions and alert the authorized entrants if the ventilation system fails.
  Attendants will ensure appropriate and approved respiratory protection equipment including breathing air remains available for immediate use.

## Slide 9: Attendant
Rescue
  Attendants shall not enter permit-required confined spaces to attempt the rescue of Authorized Entrants.
  Attendants may only perform or assist in rescue efforts if trained in the use of rescue equipment AND if replaced by another qualified attendant.

## Slide 10: Summary of Attendant Roles
Knows the hazards of entry
Knows the signs and symptoms of exposure
Maintains accurate account of entrants in space
Remains outside of space until or unless relieved
Communicates with entrants as needed
Monitors the space to determine if it remains safe
Summons rescue or emergency services

## Slide 12: CSB Video Discussion
Use 5 why’s to identify possible root causes.
  What went wrong?
  What were the false choices that were made?
  What do you think the cost of this accident was?
    List direct and indirect costs.
  What should have been done?

## Slide 13: Personal Protective Equipment
Attendants will be provided with:
Monitoring Equipment
Protective Clothing
Oxygen
Respirator
Safety Glasses
Air Purifying
SAR/SCBA
Harness for entrants
Steel-toed Boots
Retrieval Line
Rescue Hoisting Device
LEL/LFL
Toxicity

## Slide 14
All workers involved in confined space entry must be appropriately trained – it is important that confined space rescues are only done by workers who are properly trained and equipped
DO NOT ATTEMPT A RESCUE UNLESS YOU ARE PROPERLY TRAINED, EQUIPPED AND SUPPORTED.

## Slide 15: Course References
29CFR1910.120 Hazardous Materials
29CFR1910.146 Confined Space
29CFR1910.134 Respiratory Protection
29CFR1910.147 Control of Hazardous Energy (LOTO)
29CFR1910.1000 Air Contaminants
ANSI/ASSP Z117.1-2016 Safety Requirements for Entering Confined Spaces