## Slide 1
Confined Space Training
“Entry Supervisor”
Designed for employees who serve as Entry Supervisors
under the permit required confined space program.
Effective Date: February 28, 2019
Notes: The objective of the site Confined Space Entry program is to have a system for identifying Confined Spaces, evaluating the potential hazards associated with these spaces and developing hazard controls and safe entry procedures. The Confined Space program shall provide systematic approaches to protect employees from hazards associated with working inside equipment or other places with limited room or access. Whenever possible, Confined Space work shall be avoided, but when it is necessary, strict adherence to the provisions of this program is required.

## Slide 2: Course Objectives
The goal of this course is to help Entry Supervisors understand their role in creating a safe, permit-required confined space entry.
Our aim is to provide each student with the knowledge, tools, procedures and specific processes that will ensure all permit-required confined space entries are conducted safely.
Prerequisites: Entrant Training
Attendant Training

## Slide 3: Summary of Entry Supervisor Role
Evaluates the Site Conditions
Oversees Entry Conditions
Authorizes Entry or Allows Entry to Continue
Takes Measures to Protect Personnel
Has Authority to Terminate the Entry

## Slide 4: Entry Supervisor
Entry Supervisors are responsible for authorizing Permit-Required Confined Space Entry by:
  Determining that the entry permit is complete before authorizing or allowing entry.
  Determining that necessary procedures, practices and equipment are in effect for safe entry.
  Determined that entry operations remain consistent with the terms of the entry permit and that acceptable entry conditions are present.

## Slide 5: Entry Supervisor
  Cancel the entry authorization and terminate entry whenever acceptable entry conditions are not present.
  Verify that rescue services are available and the means for summoning them are operable.
  Ensure that rescue personnel and equipment are available to perform rescue duties as required.
  Ensure that barriers to entry are set-up around the opening and that unauthorized equipment is removed from the permit required confined space.

## Slide 6: Entry Supervisor
  Take the necessary measures for concluding and entry operation, such as closing the permit-required confined space, canceling the permit, and completing the information on the reverse side of the permit.
  Entry Supervisors may serve as Authorized Entrants or Attendants for an entry if they have received the proper training.
  Entry Supervisors must not leave the plant site while entry is in progress unless relieved by another qualified entry supervisor.
  Entry Supervisors will take charge in removing unauthorized individuals who attempt to enter permit-required confined spaces.

## Slide 7: Entry Supervisor Responsibilities
Knows the Hazards the Entry Team may face
Know the Signs and Symptoms of exposure
Removes unauthorized individuals
Transfers responsibility to other entry supervisors
Cancels the Entry Permit

## Slide 8
Chemicals Safety Board
Confined Space Accident

## Slide 9: CSB Video Discussion
Use 5 why’s to identify possible root causes.
  What went wrong?
  What were the false choices that were made?
  What do you think the cost of this accident was?
    List direct and indirect costs.
  What should have been done?

## Slide 10: Personal Protective Equipment
Entry Supervisors will be provided with:
Monitoring Equipment
Protective Clothing
Oxygen
Respirator
Safety Glasses
Air Purifying
SAR/SCBA
Harness for Entrant
Steel-toed Boots
Retrieval Line
Rescue Hoisting Device
LEL/LFL
Toxicity

## Slide 11: Permit Issuer
Permit issuers for confined space entry permits are:
  Responsible for issuing the confined space permit.
  Ensure all permit requirements have been met and all permit items are completed.
  Understands and reviews work to be performed, hazards, special precautions necessary and duties and requirement with entry supervisor, attendant, and entrants.
  Ensures that rescue services are available before issuing permit.

## Slide 12
All workers involved in confined space entry must be appropriately trained – it is important that confined space rescues are only done by workers who are properly trained and equipped
DO NOT ATTEMPT A RESCUE UNLESS YOU ARE PROPERLY TRAINED, EQUIPPED AND SUPPORTED.

## Slide 13: Course References
29CFR1910.120 Hazardous Materials
29CFR1910.146 Confined Space
29CFR1910.134 Respiratory Protection
29CFR1910.147 Control of Hazardous Energy (LOTO)
29CFR1910.1000 Air Contaminants
ANSI/ASSP Z117.1-2016 Safety Requirements for Entering Confined Spaces